## Slide 1
Great Lakes Navigation Challenges: A USACE Perspective
Josh Feldmann
U.S. Army Corps of Engineers Chief, Operations, Buffalo District
August 30, 2016

## Slide 2
Great Lakes Navigation System Economic Data
A non-linear interdependent system of 140 deep and shallow draft projects; commercial ports are dependent on each other for the efficiency and health of the system.
145M tons (5-year average) – (USACE Waterborne Commerce Statistics)
20% of tonnage is exported – to Canada or overseas (USACE Waterborne Commerce Statistics)
GLNS saves the country $3.6 billion per year compared to the next least costly mode of transportation (USACE Inland Nav Center of Expertise)
Notes: 140 projects – next slide will show details on geographic extent of system
Most tonnage is internal to the GL. US-US or US-Canada. A majority of the cargo consists of bulk commodities being transported from source generally on Lake Superior (mines, etc) to destination manufacturing center (mills, power plants, etc) on the lower lakes
$3.6B a year over next least costly mode of transportation; According to Marad’s recent report (Feb 2013), studies have demonstrated that, on average, transportation cost savings from $10 to more than $20 per ton of bulk cargo are associated with the use of Lakers compared to the next most competitive transportation mode (rail or truck).
The GLNS is extremely important to the nation and especially to the manufacturing industry in this country

## Slide 3
Ogdensburg
Lake Superior
Lake Michigan
Lake Huron
Lake Erie
Lake
Ontario
MI
MI
NY
PA
IL
WI
IN
CANADA
OH
Morristown
Cape Vincent
Sackets Harbor
Port Ontario
Oswego
Little Sodus Bay
Great Sodus Bay
Irondequoit Bay
Rochester
Oak Orchard
Olcott
Wilson
Little River
Black Rock Lock/Tonawanda
Buffalo
Sturgeon Point
Cattaraugus
Dunkirk
Barcelona
Erie
Ashtabula
Conneaut
Fairport
Cleveland
Rocky River
Lorain
Vermilion
Huron
Sandusky
West Harbor
Port Clinton
Toussaint River
Cooley Canal
Toledo
Put-In-Bay
Bolles Harbor
Monroe
Rouge River
Detroit River
Clinton River
Belle River
Pine River
Lake St. Clair
St. Clair River
Black River
Lexington
Caseville
Port Austin
Bay Port
Harbor Beach
Port Sanilac
Sebewaing
Saginaw
Point Lookout
Tawas Bay
Au Sable Harbor
Harrisville
Alpena
Hammond Bay
Cheboygan
Inland Route
Mackinac City
Mackinac Island
St. James
Petoskey
Charlevoix
Channels in Straits of Mackinac
Grays Reef
Leland
Greilickville
Frankfort
Arcadia
Portage Lake
Manistee
Ludington
Pentwater
White Lake
Muskegon
Saugatuck
Grand River
Holland
Grand Haven
South Haven
St. Joseph
St. Joseph River
New Buffalo
Michigan City
Burns Small Boat Harbor
Burns Waterway Harbor
Indiana Harbor
Calumet
Chicago River
Chicago Harbor
Waukegan
Kenosha
Milwaukee
Port Washington
Sheboygan
Manitowoc
Washington Island
Green Bay
Big Suamico
Kewaunee
Algoma
Sturgeon Bay
Two Rivers
Pensaukee
Oconto
Menominee
Cedar River
Little Bay de noc
Manistique
Detour
Les Cheneaux Island
Soo Locks
St. Marys River
Whitefish Point Harbor
Little Lake
Grand Marais
Presque Isle
Marquette
Big Bay
Grand Traverse Bay
Lac La Belle
Eagle Harbor
Keweenaw Waterway
Ontonagon
Black River
Saxon
Ashland
Chippewa Harbor
Grand Marais
Silver Bay
Two Harbors
Knife River
Duluth-Superior
Bayfield
La Pointe
Cornucopia
Port Wing
Commercial
Recreational
Federal Projects on the Great Lakes
A non-linear navigation system with 60 federal commercial projects and 80 federal shallow draft/recreational projects
Taconite
Niagara River
3
Notes: Great Lakes system is comprised of:
140 federal harbors on the great lakes: 60 commercial and 80 recreational
Connecting channels: St. Marys, Detroit River, St. Clair River, and Channels of Lake St. Clair
3 locks: Soo, Chicago, Black Rock (Buffalo)
We maintain the channels (dredging) and also maintain the navigation structures at each harbor.

## Slide 4
Lake Superior
Lake Michigan
Lake Huron
Lake Erie
MI
MI
NY
PA
IL
WI
IN
CANADA
OH
Alpena
Chicago Harbor
Green Bay
Duluth-Superior
Rouge River
Detroit River
Calumet
Grand Haven
Monroe
Fairport
Cleveland
Toledo
Burns Waterway Harbor
Indiana Harbor
Ludington
Milwaukee
Two Harbors
Silver Bay
Charlevoix
Buffalo
Huron
Sandusky
Muskegon
Presque Isle
Marquette
Ashland
Saginaw
Ashtabula
Conneaut
Lorain
Harbor Beach
Manistee
Manitowoc
Cheboygan
Marysville
St. Joseph
Waukegan
Put In Bay
Menominee
Ontonagon
Gladstone
Holland
St. Clair
Lake
Ontario
>10M Ton Harbor 1-10M Ton Harbor <1M Ton Harbor
Key Challenges
Balancing System Requirements
  Dredging
  Dredged Material Management
  Navigation structures
  Soo Locks
Interdependency requires using a system approach in prioritizing investments
Great Lakes Navigation
Interdependent Ports
Notes: - GL is a system of interdependent ports
High tonnage harbors are dependent on low and moderate tonnage harbors
There are four main categories to our Nav mission on the GL: dredging, dredged material management, navigation structures, locks
Must consider interrelationship of harbors in prioritizing projects – Managing the GL as a system is key to our approach

## Slide 5: Dredging
Notes: Pictures of 2009 dredging at Lorain Harbor (left) and Kewaunee Harbor (right)

## Slide 6
Ogdensburg
Lake Superior
Lake Michigan
Lake Huron
Lake Erie
Lake
Ontario
MI
MI
NY
PA
IL
WI
IN
CANADA
OH
Morristown
Cape Vincent
Sackets Harbor
Port Ontario
Oswego
Little Sodus Bay
Great Sodus Bay
Irondequoit Bay
Rochester
Oak Orchard
Olcott
Wilson
Little River
Black Rock Lock/Tonawanda
Buffalo
Sturgeon Point
Cattaraugus
Dunkirk
Barcelona
Erie
Ashtabula
Conneaut
Fairport
Cleveland
Rocky River
Lorain
Vermilion
Huron
Sandusky
West Harbor
Port Clinton
Toussaint River
Cooley Canal
Toledo
Put-In-Bay
Bolles Harbor
Monroe
Rouge River
Detroit River
Clinton River
Belle River
Pine River
Chnls Lake St. Clair
St. Clair River
Black River
Lexington
Caseville
Port Austin
Bay Port
Harbor Beach
Port Sanilac
Sebewaing
Saginaw
Point Lookout
Tawas Bay
Au Sable Harbor
Harrisville
Black River Harbor
Alpena
Hammond Bay
Cheboygan
Inland Route
Mackinac City
Mackinac Island
St. James
Petoskey
Charlevoix
Channels in Straits of Mackinac
Grays Reef
Leland
Greilickville
Frankfort
Arcadia
Portage Lake
Manistee
Ludington
Pentwater
White Lake
Muskegon
Saugatuck
Grand River
Holland
Grand Haven
South Haven
St. Joseph
St. Joseph River
New Buffalo
Michigan City
Burns Small Boat Harbor
Burns Waterway Harbor
Chicago River
Chicago Harbor
Waukegan
Kenosha
Milwaukee
Port Washington
Sheboygan
Manitowoc
Washington Island
Green Bay
Big Suamico
Kewaunee
Algoma
Sturgeon Bay
Two Rivers
Pensaukee
Oconto
Menominee
Cedar River
Little Bay de noc
Manistique
Detour
Les Cheneaux Island
Soo Locks
St. Marys River
Whitefish Point Harbor
Little Lake
Grand Marais
Presque Isle
Marquette
Big Bay
Grand Traverse Bay
Lac La Belle
Eagle Harbor
Keweenaw Waterway
Black River
Saxon
Ashland
Chippewa Harbor
Grand Marais
Two Harbors
Knife River
Duluth-Superior
Bayfield
La Pointe
Cornucopia
Port Wing
FY16 Dredging Funding and Dredging Requirements
Calumet
Indiana Harbor
Commercial
Recreational
Ontonagon
Silver Bay
Taconite
FY16 Unbudgeted Dredging Need
FY16 Funded Dredging
Notes: Green dots show harbors that are funded in FY15 in PB. Note that many (probably all) harbors are not funded to their full need due to highly constrained budgets. There are 23 projects funded in FY15.

## Slide 7: FY16 PBUD + Work Plan Dredging ($59.2M)
Duluth-Superior +
Green Bay +
Erie
Indiana Harbor
Holland
Grand Haven
Saginaw River +
Ludington
Toledo
Presque Isle
Rouge River
Manistee
Conneaut
Sandusky
Cleveland
Alpena
Fairport
Huron
Waukegan
Burns Harbor
Monroe
Rochester
St. Joseph
Muskegon
Calumet +
Ontonagon
Lorain
Manistique
Manitowoc
Oswego

## Slide 8: FY 17 Great Lakes Navigation
$103.3M Great Lakes Navigation Operations & Maintenance
Key Items
$39M in Dredging (19 projects – 3.2M cubic yards)
$8.2M in Dredged Material Management
$5.9M in Soo Asset Renewal

## Slide 9
Ogdensburg
Lake Superior
Lake Michigan
Lake Huron
Lake Erie
Lake
Ontario
MI
MI
NY
PA
IL
WI
IN
CANADA
OH
Morristown
Cape Vincent
Sackets Harbor
Port Ontario
Oswego
Little Sodus Bay
Great Sodus Bay
Irondequoit Bay
Rochester
Oak Orchard
Olcott
Wilson
Little River
Black Rock Lock/Tonawanda
Buffalo
Sturgeon Point
Cattaraugus
Dunkirk
Barcelona
Erie
Ashtabula
Conneaut
Fairport
Cleveland
Rocky River
Lorain
Vermilion
Huron
Sandusky
West Harbor
Port Clinton
Toussaint River
Cooley Canal
Toledo
Put-In-Bay
Bolles Harbor
Monroe
Rouge River
Detroit River
Clinton River
Belle River
Pine River
Chnls Lake St. Clair
St. Clair River
Black River
Lexington
Caseville
Port Austin
Bay Port
Harbor Beach
Port Sanilac
Sebewaing
Saginaw
Point Lookout
Tawas Bay
Au Sable Harbor
Harrisville
Black River Harbor
Alpena
Hammond Bay
Cheboygan
Inland Route
Mackinac City
Mackinac Island
St. James
Cross Village
Petoskey
Charlevoix
Channels in Straits of Mackinac
Grays Reef
Leland
Greilickville
Frankfort
Arcadia
Portage Lake
Manistee
Ludington
Pentwater
White Lake
Muskegon
Saugatuck
Grand River
Holland
Grand Haven
South Haven
St. Joseph
St. Joseph River
New Buffalo
Michigan City
Burns Small Boat Harbor
Burns Waterway Harbor
Chicago River
Chicago Harbor
Waukegan
Kenosha
Milwaukee
Port Washington
Sheboygan
Manitowoc
Washington Island
Green Bay
Big Suamico
Kewaunee
Algoma
Sturgeon Bay
Two Rivers
Pensaukee
Oconto
Menominee
Cedar River
Little Bay de noc
Gladstone
Manistique
Detour
Les Cheneaux Island
Soo Locks
St. Marys River
Whitefish Point Harbor
Little Lake
Grand Marais
Presque Isle
Marquette
Big Bay
Grand Traverse Bay
Lac La Belle
Eagle Harbor
Keweenaw Waterway
Black River
Saxon
Ashland
Chippewa Harbor
Grand Marais
Beaver Bay
Two Harbors
Knife River
Duluth-Superior
Bayfield
La Pointe
Cornucopia
Port Wing
FY17 President’s Budget Dredging Projects
Calumet
Indiana Harbor
Commercial
Recreational
President’s Budget
Ontonagon

## Slide 10: Historical Shallow Draft/Recreational Harbor Funding
Chart: Fiscal Year
| 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
Number | 29 | 19 | 21 | 17 | 15 | 11 | 0 | 24 | 18 | 17 | 0 | 0 | 0 | 6 | 0

Notes: Many members ask about funding for recreational harbors.
Although 2014 and 15 are good funding years for GL, the news is not so positive for the recreational harbor stakeholders. With funds so limited and the many needs throughout the country, the Corps prioritizes projects that support commercial shipping.
Number of projects includes dredging and structural repair – only regular Corps funding – no contributed funds, no Sandy funds
Shallow Draft/Recreational: harbors that are authorized as deep draft but with no commercial traffic are included in the Rec count.
Background
Last time rec harbors were in PB was 2006 (Lac La Belle)
2007 and 2011 year long CR – only PB projects
2008, 2009, 2010 Adds , regional provisions and ARRA
2012 – had appropriation with additional funds for ongoing work but no funds were allocated to rec harbors
- no funding other than Sandy and state of MI contributed funds so 0 in this table.
2014 funding for rec harbors 5 dredging and 1 structure repair (including authorized deep draft with no comm traffic) funded in “additional funds for ongoing work”

## Slide 11: Dredged Material Management

## Slide 12
Historical Perspective
1970
1980
1990
Dredged material nearly exclusively disposed via open water placement
1970 - River and Harbor Act and Flood Control Act of 1970 (PL 91-611) passed
1988 - Federal Standard defined
1996 - Section 201 of the 1996 WRDA requires cost-sharing
1960
2000
45 Great Lakes CDFs constructed and/or operated by USACE at a cost of $900M (2009 dollars)
Current CRITICAL situation. DMM strategies must be developed.
Execute sustainable DMM solutions
Notes: December 1970: In December of 1970, Congress passed the River and Harbor and Flood Control Act of 1970 (P.L. 91-611). Section 123 of that Act specifically authorized the USACE to construct, operate and maintain “spoil disposal” facilities on the Great Lakes for the confinement of dredged materials. Costs of facilities were to be borne by the federal government and a non-federal sponsor. The need for a particular CDF was to be established in conjunction with the USEPA and the affected states and local entities. Further, Section 123 stated that spoil facilities were to be established for a period not to exceed 10 years. The assumption at the time was that after 10 years, the nation’s waters would be sufficiently restored such that dredged material would no longer require confined disposal. Amendments to that authority extended the timeframe in which CDFs could continue to be operated by the Corps.
1970 to Present: Most of this construction occurred between 1974 and 1980. There are currently 20 active CDFs on the Great Lakes, which are more than 80 percent full.
1988: The Federal Standard (33 CFR 209, 335-338) is the least costly management alternative that is technically sound and complies with federal environmental laws and regulations. If a state or local government imposes restrictions that are more costly than the Federal Standard, the additional costs must be borne by non-federal interests. The Federal Standard levels the playing field for dredging and related costs among states having disparate policies and requirements on dredged material management. A state that may wish to have a policy prohibiting open water disposal regardless of testing and evaluation of its suitability will have to pay all costs beyond those associated with the Federal Standard. The USEPA/USACE testing protocol that defines the “Federal Standard” is currently under revision, with the updated dredged material testing standards for open water disposal to take effect in 2011. Those standards are expected to be even more stringent than those that exist today, further limiting disposal options.
1996: Section 201 of the Water Resources Development Act of 1996 created a national program for the construction of CDFs. This authority specified uniform cost-sharing requirements for all future CDFs. The non-federal cost share is based on the depth of the navigation channel. For deep draft channels on the Great Lakes (greater than 18 feet and less than 45 feet), the non-federal sponsor must provide 25 percent of CDF construction costs, plus an additional 10 percent (paid over as long as 30 years) against which all lands, easements, rights-of-way and relocations may be credited.

## Slide 13: Navigation Structures

## Slide 14: Great Lakes Navigation Structures - Purposes
Navigation structures intended purposes:
Safeguard navigation from wave and ice damage (GL experience waves over 25 ft)
Protect navigation channel from sediment shoaling
Protect navigation channel from wave action (preserve the design wave climate to allow pilots to navigate the channel)
Additional benefits provided:
Protect other navigation structures within harbor such as CDFs
Protect critical city infrastructure (buildings, roads, power plants, water/wastewater plants)
Provide essential flood and storm protection
Control wave climate within navigation channel and harbor
Control and reduce shoaling in navigation channel
Notes: Breakwater maintenance preserves the design wave climate and provides a predictable and reliable and water column for marine pilots to navigate. The loss of a predictable water column has the same economic consequences as shoaling. The harbors will not function indefinitely without regular breakwater maintenance, and a "fix as fails" approach is extremely expensive.
Increased wave climate in a harbor is unsafe for ships. Example of Burns harbor with 9 barges and 1 tug sinking in the harbor in March 1998 and three vessels sinking within the harbor in the 1970s due to deficiencies in the breakwater (sections that had lost 2 to 3 feet of design height caused waves climate in the harbor to increase to a point that barges became unstable and sank); ERDC report documented the unusual amount of stone replacement maintenance needed at Burns due to the strength of the wave s and ice that routinely pound the structure.
Higher waves in a harbor will also force vessels to lighten their load even more. Thus, increased waves in a harbor have the same effect as increased shoaling in terms of economic consequences resulting from light loading.
Dredging is how the Corps controls available water depth in a channel; Coastal structures are how the Corps controls the wave climate in a harbor – both affect the safe navigability of the vessel and the amount of light loading required.

## Slide 15: Great Lakes Navigation Structure Conditions
50% of GL coastal structures were built before WWI
Over 80% of all coastal structures exceed 50 years of age
45% have never undergone any significant repair effort due to funding constraints
Over 30% of structures have timber crib core sections; recent low water levels have accelerated deterioration of the wood
Notes: Left : Calumet steel sheet pile crumpled and twisted due to wave action
Middle: Fairport – significant loss of stone – ability to restrain waves is significantly compromised
Right: Chicago harbor – loss of height and shifting stone and cap

## Slide 16: Harbor Structure Condition Assessments
Lake Superior
Lake Michigan
Lake Huron
Lake Erie
Lake
Ontario
MI
MI
NY
PA
IL
WI
IN
CANADA
OH
Oswego
Rochester
Black Rock Lock/Tonawanda
Buffalo
Dunkirk
Erie
Ashtabula
Conneaut
Fairport
Cleveland
Lorain
Huron
Sandusky
Detroit River
Harbor Beach
Alpena
Cheboygan
Charlevoix
Frankfort
Manistee
Ludington
Muskegon
Holland
Grand Haven
South Haven
St. Joseph
Michigan City
Burns Waterway Harbor
Calumet
Indiana Harbor
Chicago River
Chicago Harbor
Waukegan
Kenosha
Milwaukee
Port Washington
Sheboygan
Manitowoc
Kewaunee
Algoma
Sturgeon Bay
Menominee
Manistique
Detour
Grand Marais
Presque Isle
Marquette
Keweenaw
Waterway
Ontonagon
Ashland
Two Harbors
Knife River
Duluth-Superior
Burns Small Boat Harbor
Bolles Harbor
Au Sable
Caseville
Hammond Bay
Harrisville
Lexington
Mackinac Island
Mackinaw City
Point Lookout
Port Austin
Port Sanilac
Tawas Bay
Arcadia
Greilickville
Inland Route
Leland
New Buffalo
Pentwater
Petoskey
Portage Lake
Saugatuck
White Lake
Clinton River
Big Bay
Black River
Eagle Harbor
Grand Traverse
Lac La Belle
Little Lake
Whitefish Point
Grand Marais
Barcelona
Cattaraugus
Great Sodus Bay
Irondequoit Bay
Little Sodus Bay
Oak Orchard
Olcott
Port Ontario
Wilson
Cape Vincent
Cooley Canal
Port Clinton
Vermilion
West Harbor
Rocky River
Oconto
Two Rivers
Bayfield
Cornucopia
La Pointe
Port Wing
Saxon
Cedar River
Commercial
Recreational
A – Failure Unlikely
B – Low Risk of Failure C – Medium Risk of Failure
D – High Risk of Failure
F – Failed
Cost to Restore Most Critical Harbors to Acceptable Level of Risk:
Ashtabula Harbor
$39.0M
Chicago Harbor
$19.6M
Cleveland Harbor
$10.0M
Fairport Harbor
$28.0M
Lorain Harbor
$14.0M
Milwaukee Harbor
$33.0M
________________
Total: $143.6M
Notes: There are over 130 coastal cities and towns on the Great Lakes with federal navigation projects that include breakwaters; 63 of these projects currently support commercial navigation. Originally built to safeguard navigation in the federal harbors from waves and ice, these structures also provide critical flood and storm damage protection for buildings, roads, facilities and municipal infrastructure. In many cases, cities and downtowns have ‘grown up’ behind and are now safeguarded by federal breakwaters.
Over 50 percent of the coastal structures on the Great Lakes were built prior to World War I (1918) and 80 percent are older than their typical 50-year design life. Federal funding for maintenance of projects is prioritized based on economic benefits related to commercial navigation. Federal breakwaters at harbors with small amounts of commercial navigation are a low priority for funding. Funding for structure repairs at harbors with significant levels of commercial navigation has also been under funded for the last decade. The Corps’ floating plant performs some preventive maintenance and minor repairs but does not have the capacity to perform major repairs or reconstruction.
The GLNS has approximately $50 million in annual needs for structure repairs. The majority of these needs represent significant repairs or reconstruction of navigation structures. In 2007 the three Great Lakes Districts formed a regional, multi-disciplined breakwater assessment team that developed technical assessment criteria and began inspecting and rating breakwaters around the Great Lakes. The breakwater assessment team’s work will allow the Corps to prioritize these needs on a regional level so that the most urgent structures are given priority in the budget process each year.
This slide demonstrates the different ratings that each of the harbor infrastructures received from the Condition Assessments. As you can see, three harbors have structures that have failed and 10 others are considered to be in high risk of failure. Out of the 13 harbors that were rated as already failed or in high risk of failure, 8 are commercial harbors. The cost to restore a few of the major harbors into an acceptable state has also been provided on this slide.

## Slide 17: Lock Reliability

## Slide 18: The Soo Locks Lynch Pin of the Great Lakes Navigation System
70% of the commercial commodities transiting the Soo Locks are limited by size to the Poe Lock
  Aging and deteriorating infrastructure; unscheduled outages increasing
  There is currently no redundancy for the Poe Lock
  The economic impact of a 30-day
  unscheduled closure of the Soo Locks = $160M
Two major efforts are underway to improve reliability of the Soo Locks
  Maintain existing infrastructure through Asset Renewal Plan
  New lock with the same dimensions as the Poe Lock - BCR sensitivity analysis underway

## Slide 19: GL Navigation Funding History
Chart: Fiscal Year
| 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016
President's Budget | 93125 | 89286 | 92956 | 90015 | 79957 | 85906 | 94940 | 102500 | 111580
Adds and National Provisions | 29423 | 24255 | 4344 | -215 | 7343 | -2413 | 23000 | 16300
ARRA | 0 | 72300 | 1700 | 0 | 0 | 0 | 0 | 0
Sustainable Funding Range
Notes: Good news story – 2014 and 2015 healthy funding, recovering from low budget years 2010 – 2013 that coincided with low water levels.

## Slide 20
20
Great Lakes Navigation System’s Transporting Rates Savings
$3.6 BILLION/year for a $90 Million/yr total investment!
More competitive American steel
Lower cost energy
Lower cost concrete (construction)
More competitive Grain for Export
Less fuel consumption and greenhouse gas emissions
Less congested highways/rails
Great Lakes Navigation System – A Great Investment
Notes: 20

## Slide 21
Questions