## Slide 1: Florida Statewide LiDAR Assessment
For
NOAA Hydrographic Services Review Panel
by
Dr. David Maune
Dewberry Consultants LLC
September 13, 2017

## Slide 2: Goals of the Florida Assessment
To identify Business Uses and their requirements and benefits for topographic LiDAR, bathymetric LiDAR and/or topobathymetric LiDAR in the state of Florida when considering potential LiDAR Quality Levels and Update Frequencies
To determine implementation scenarios that would provide the highest net benefits, using benefit-cost analysis, when considering current and emerging LiDAR technologies
To identify potential funding partnerships (to get $51M total over a 3-5 year update cycle)
(Assumed) to update changes relevant to Florida since the National Enhanced Elevation Assessment (NEEA)
(Un-stated) to serve as a pilot for an upcoming 3D Nation Requirements and Benefits Study for NOAA and USGS.

## Slide 3: NEEA’s Highest Net Benefits for Federal Government Agencies only

## Slide 4: NEEA’s Highest Net Benefits for State Government Agencies Only

## Slide 5: NEEA’s Highest Net Benefits for Non-Governmental Organizations only

## Slide 6: NEEA’s Highest Net Benefits for Combined (Federal + State + Nongovernmental)

## Slide 7: Synergy from all working together to satisfy common needs from the NEEA
If all three user groups worked alone, their total annual costs, benefits and B/C ratio would be as highlighted in yellow
But by combining their efforts in the NEEA, the annual costs, benefits and B/C ratio was as highlighted in green
All statistics in green are better than those in yellow, i.e., costs are lower and benefits are higher from partnerships
If Florida acted alone, it would justify QL5 updated 6-10 years; by acting together, the NEEA justified QL2 updated 6-10 years.

## Slide 8: Standard Business Uses (BU’s)
BU 1, Natural Resources Conservation | BU 16, Sea Level Rise & Subsidence
BU2, Water Supply & Quality | BU 17, Wildfire Management, Plan, Response
BU 3, River/Coastal Ecosystem Management | BU 18, Homeland Security, Disaster Response
BU4, Coastal Zone Management | BU 19, Land Navigation & Safety
BU 5, Forest Resources Management | BU 20, Marine/Riverine Navigation & Safety
BU 6, Rangeland Management | BU 21, Aviation Navigation & Safety
BU 7, Wildlife and Habitat Management | BU 22, Infrastructure/Construction Mgt.
BU 8, Agriculture & Precision Farming | BU 23, Urban and Regional Planning
BU 9, Aquaculture & Fish Farming | BU 24, Health and Human Services
BU 10, Geologic Resource Assessment, Haz Mit | BU 25, Real Estate, Banking, Mortgage, Insure
BU 11, Resource Mining | BU 26, Education; Basic Research
BU 12, Renewable Energy Resources | BU 27, Recreation
BU 13, Oil and Gas Resources | BU 28, Telecommunications
BU 14, Cultural Resources Preservation | BU 29, Military
BU 15, Flood Risk Management | BU 30, Maritime & Land Boundary Mgt.

## Slide 9: Topographic LiDAR Current Status
Scenario 1:
Covers topo LiDAR only

## Slide 10: Bathymetry area for Scenario 2
Scenario 2:
Covers topobathy LiDAR for nearshore bathymetry only, shown in blue.
Based on relative areas, dollar benefits reduced to 20.2% for any MCA that requires topobathy for both inland and coastal bathymetry because inland bathy unreliable in turbid waters. Consider inland bathy on case-by-case basis

## Slide 11: Questionnaire
Contact Information, organization, and program supported
User-defined Mission Critical Activity (MCA) & standard Business Uses
Geographic Area of Interest, from pick-lists or by submitting shapefiles
Topo LiDAR Quality Level and Update Frequency required for MCA
Bathy LiDAR Quality Level and Update Frequency required for MCA
Annual dollar benefits if you receive the QL and UF required for MCA
Questions to clarify LiDAR requirements and uses, deliverables, “buy- up” options, LiDAR derivatives
Questions to clarify need for dataset integration and types of integration
Questions to clarify benefits, even when dollar benefits cannot be estimated (operational, customer service, societal, environmental)
Benefit split between topo and bathy LiDAR (asked subsequently during follow-up interviews)

## Slide 12: Major Questionnaire Metrics
Participants and Benefits | Metric
Number of LiDAR stakeholders/users invited | 190
Number who opened the questionnaire and provided contact information | 104
Number who provided LiDAR requirements (MCA, AOI, Quality Level (QL) and Update Frequency (UF) | 78
Number of Mission Critical Activities (MCAs) documented | 97
Number of 97 documented MCAs with Dollar Benefits | 64
Number with Topographic LiDAR Benefits | 64
Number with Bathymetric LiDAR Benefits | 48
Total Current Topo LiDAR Annual Benefits for all MCAs | $45M - $49M
Total Future Topo LiDAR Additional Annual Benefits if all MCAs receive the Topo QL and UF requested | $31M - $44M
Total Future Bathy LiDAR Additional Annual Benefits if all MCAs receive the Bathy QL and UF requested | $66M - $72M
NOTE: These dollar benefits will degrade for scenarios with poorer QL and/or UF
$29.52M
$35.17M

## Slide 13: Topographic LiDAR Quality Levels (QLs)
Quality Level (QL) | Aggregate Nominal Pulse Spacing (ANPS) (m) | Aggregate Nominal Pulse Density (ANPD) (points/m2) | RMSEz (non-vegetated) (cm) | NVA at 95% confidence level (cm) | VVA at 95th percentile (cm)
QL0 | ≤0.35 | ≥8 | ≤5 | ≤9.8 | ≤14.7
QL1 | ≤0.35 | ≥8 | ≤10 | ≤19.6 | ≤29.4
QL2 | ≤0.71 | ≥2 | ≤10 | ≤19.6 | ≤29.4
Primary Issue: What should be the reduced value multiplier for any scenario where a Mission Critical Activity receives a poorer Quality Level than required? We tried many alternatives, with sensitivity analysis, and decided on a hybrid model based on cost differences between QL0 & QL1 and NEEA’s 0.5 multiplier between QL1 & QL2.
Secondary Issue: What should be the reduced value multiplier for any scenario where a Mission Critical Activity receives a poorer Update Frequency than required? We decided to retain the 0.5 multiplier that worked well for the NEEA study.

## Slide 14: Topo LiDAR Reduced Value Multipliers for hybrid model
Quality Level required | If QL0 Received | If QL1 Received | If QL2 Received
QL0 | 1.0 | 0.8659 | 0.4329
QL1 | 1.0 | 1.0 | 0.5
QL2 | 1.0 | 1.0 | 1.0
QL1 costs/QL0 cost difference = 0.8659
QL2 is degraded by 0.5 relative to QL1 (consistent with the NEEA)

## Slide 15: How the Update Frequency 0.5 Multipliers Work
Update Frequency required for $100,000 annual benefits | Annual update scenario annual benefits received | 2-3 year update scenario annual benefits received | 4-5 year update scenario annual benefits received | 6-10 year update scenario annual benefits received | >10 year update scenario annual benefits received
Annual | $100,000 | $50,000 | $25,000 | $12,500 | $6,250
2-3 years | $100,000 | $100,000 | $50,000 | $25,000 | $12,500
4-5 years | $100,000 | $100,000 | $100,000 | $50,000 | $25,000
6-10 years | $100,000 | $100,000 | $100,000 | $100,000 | $50,000
>10 years | $100,000 | $100,000 | $100,000 | $100,000 | $100,000
Event Driven | $50,000 | $50,000 | $50,000 | $50,000 | $50,000

## Slide 16: Scenario 1: Statewide Topo LiDAR, highest Net Benefits if updated every 2-3 years

## Slide 17: Topo LiDAR Scenario 1 Conclusions

## Slide 18: County-by-county assessment with highest Topo LiDAR Net Benefits
1 MCA
$1.2M
QL0
2-3 years
1 MCA
$1M
QL0
2-3 years
1 MCA
$280K
QL0
4-5 years
1 MCA
$150K
QL0
4-5 years
Other counties largely misleading because only 8 counties submitted LiDAR requirements and benefits

## Slide 19: Bathymetric LiDAR Quality Levels (QLB)
 | QL0B | QL1B | QL2B | QL3B | QL4B
Nominal Pulse Spacing | ≤0.7m | ≤2.0 m | ≤0.7 m | ≤2.0 m | ≤5.0 m
Nominal Pulse Density | ≥2.0 pts/m2 | ≥0.25 pts/m2 | ≥2.0 pts/m2 | ≥0.25 pts/m2 | ≥0.04 pts/m2
Depth Examples | Vertical Accuracy of submerged elevations at 95% Confidence Level (cm) |  |  |  | 
0 m | 25.0 | 25.0 | 30.0 | 30.0 | 50.0
10 m | 26.1 | 26.1 | 32.7 | 32.7 | 51.7
20 m | 29.2 | 29.2 | 39.7 | 39.7 | 56.4
Applications | Detailed site surveys requiring the highest accuracy and highest resolution seafloor definition; dredging and inshore engineering surveys; high-resolution surveys of ports and harbors |  | Charting surveys; regional sediment management; general bathymetric mapping; coastal science and management applications; change analysis; deep water surveys; environmental analyses |  | Recon/planning; all general applications not requiring higher resolution and accuracy
Base Cost ~18% cheaper <2% cheaper ~20% cheaper ~42% cheaper
Note: significant cost difference between red/green and between green/blue
IHO Special Order

## Slide 20: Bathy reduced value multipliers based totally on cost differences
QLB Required | QL0B Received | QL2B Received | QL1B Received | QL3B Received | QL4B Received
QL0B | 1.0 | 0.9894 | 0.8507 | 0.7155 | 0.4972
QL2B | 1.0 | 1.0 | 0.8598 | 0.8411 | 0.6948
QL1B | 1.0 | 1.0 | 1.0 | 0.9783 | 0.8261
QL3B | 1.0 | 1.0 | 1.0 | 1.0 | 0.8444
QL4B | 1.0 | 1.0 | 1.0 | 1.0 | 1.0
In this table, the Quality Levels are re-ordered by cost, and QL2B is valued higher than QL1B because:
QL2B with 2 pts/m2 cost more even though 5 cm less accurate at 95%
QL1B with 0.25 pts/m2 cost less even though 5 cm more accurate at 95% confidence level (2.5 cm RMSEz difference)
Reduced value multiplier example: QL1 cost/QL2 cost = 0.8598

## Slide 21: Scenario 2: Statewide Bathy LiDAR (nearshore bathy only) using cost difference multipliers

## Slide 22: Bathy LiDAR Scenario 2 Conclusions

## Slide 23: But what if inland bathy needs cannot be met with LiDAR?

## Slide 24: Questions?