## Slide 1: Introduction to Bathymetric Lidar: Sensors, Capabilities, and Limitations
Carol Lockhart

## Slide 2: Acknowledgements
USACE/JALBTCX for allowing us to show project data images
University of New Hampshire CCOM for providing graphics

## Slide 3: Operational Concepts
Consistent swath widths
More efficient coverage in very shallow water (<5 – 15m)
Eliminates safety concerns of boat operations in shallow uncharted water
Can be combined with multibeam for optimal survey results, efficiency & safety
Sample Project >200km2
Very Shallow Depths (3m on average)
Understand limitations
Technology | Time to Survey
Full Coverage Multibeam | 1 year
100% Sidescan Sonar (with singlebeam or skunk striped bathy) | 60 days
Bathy Lidar | 2 days

## Slide 4: Bathymetric Lidar History
1st Generation (early 70’s) US: PLADS Australia: WRELADS I USSR, Sweden, Canada: Ship-borne lidar
2nd-3rd Generation (mid 70’s – late 80’s) US: AOL, HALS, ALARMS Australia: WRELADS II, RAN LADS USSR: GOI, Chaika, Markel-II Sweden: OWL, FLASH-1 Canada: CCRS, LARSEN-500, China: BLOL
Operational systems (early 90’s – today) US/Canada: SHOALS, EAARL Australia: LADS Sweden: HawkEye
Current Sensors Optech: SHOALS-3000, CZMIL, Titan Leica: HawkEye III, Chiroptera II Fugro LADS: LADS Mk III Riegl: VQ-820-G, VQ-880-G
Increased Capabilities
(higher PRF, additional Sensors, …)
Decreased Size & Weight

## Slide 5: JALBTCX Lidar Program History
200
2003
CHARTS
$ / km2
1994
SHOALS
1999
SHOALS
2012
CZMIL
Bathymetry
Topography
Photogrammetry
Spectral Imagery
Data Fusion
Measurements/Sec
400
1000
3000
10000
2005
CHARTS
Slide Courtesy of JALBTCX (2012)

## Slide 6: Current Sensors
Traditional / High-Power
(Deep Channel Systems)
  Optech SHOALS-1000/3000
  Fugro LADS Mk III
  Optech CZMIL
  Leica HawkEye III
Low-Power
(Topo-Bathy or Shallow Channel Systems)
  EAARL-B
  Optech Titan
  Leica Chiroptera II
  Riegl VQ820-G / 880G

## Slide 7: Bathy Lidar Theory
Frequency Doubled ND:YAG Class IV Laser output or Independent Lasers:
    Infrared (1064nm)
    Visible Green (532nm)
Laser fires against a scanning mirror or circular palmer scanner to create a swath of points.

## Slide 8: Bathy Lidar Theory
Green (532nm)
sea surface, water column & seafloor
IR (1064nm)
sea surface
Seafloor
Sea surface
Intensity
Seafloor
Sea surface
Intensity
Raman Return (Red 640 to 670nm)
sea surface, upper water column
Seafloor
Sea surface
Intensity

## Slide 9: Conceptual Green Waveform
(Guenther et al., 2000)

## Slide 10: Sensor Comparisons – Scan Pattern
Line Scanning
e.g. LADS Mk III
Arc Scanning
e.g. SHOALS, Riegl VQ-820-G
Elliptical Scanning
e.g. CZMIL, Chiroptera,
Riegl VQ-880-G

## Slide 11: CZMIL Hybrid Approach – Conical Scanning
x
3
2
4
0
1
5
6
Graphics Courtesy of JALBTCX (2012)

## Slide 12: Changes in Footprint Concept: Segmented Detection
2 - 3 m
2 - 3 m
SHOALS / LADS
CZMIL
2.5 - 3 m
~ 0.5 m
~ 0.5 m
SHOALS
LADS HAS NO IR
Chiroptera II / HawkEye III
Riegl VQ-820-G
~1.2m
0.4m
~ 0.2 m
~ 2 m

## Slide 13: Shallow Water Discrimination
Images Courtesy of JALBTCX (2012)

## Slide 14: CZMIL compared to SHOALS
Chart: 
Chart: Time bins(ns)
Ft. Lauderdale water, 25m (40mrad channel, Kd ≈ 0.12 m-1)
Higher Signal, Better SNR
Better (shorter) system response
P3
P4
Ft. Lauderdale, 1.5m (Kd ≈ 0.12 m-1 , Shallow water channels)
CZMIL
Better SNR and shorter system response
Detect bottom deeper
More accurate input to algorithms
Better shallow water discrimination

## Slide 15: System Response Time
Actual Chiroptera waveform at 1.2 meters depth (blue) versus simulated waveform with a 20 ns response time (green)
Chiroptera
20 ns waveform

## Slide 16: Deep v Shallow Sensors
 | Deep Channel Sensor | Shallow Channel Sensor
Flying Speed (knots) | 120-180 | 120-180
Flight Altitude (m) | 200 - 600 | 200 - 600m
Swath Width (m) | 60 - 585 | ~ 290m
Sounding Density (m) | 0.4 to 0.05 pts /m2 | 1.5 to >10 pts /m2
PRF | 1 – 10 kHz (70kHz shallow for CZMIL) | Up to 550 kHz
Min Depth (m) | 0 / 0.2m / 1.5m | 0m
Max Depth (m) * | ~ 50 – 80m 2 – 3.5 x Secchi Depth | ~ 15m 1.5 x Secchi Depth
Depth Accuracy | IHO Order 1 or Better | IHO Order 1 or Better
Horizontal Accuracy | IHO Order 1 or Better | IHO Order 1 or Better
Power | 50A – 100A @ 28 VDC | ~30A @ 18-32 VDC
Weight | 190 – 500 kg | < 100kg
Nominal Footprint Size | 2 – 3m | ~ 40cm

## Slide 17: Design Trade Off
Fixed Power
PRF
Depth Penetration

## Slide 18: Real World Accuracy Statistics
Comparing Lidar and Acoustic Bathymetry Using TPU and the CUBE Algorithm, ILMF (2008) , C. Lockhart, D. Lockhart, J. Martinez

## Slide 19: Sensors
Optech CZMIL
Control Rack
Thermal Rack
Laser Rack
Operator Rack
Lidar Sensor Head
T-4800 Camera
CASI-1500
Riegl VQ820-G
Image provided courtesy of QSI

## Slide 20: Leica Modular Sensor Design
Topo Lidar Survey
(Single or Dual-Head)
Shallow Bathy
~1.5 x Secchi depth
Deep Bathy
~3 x Secchi depth

## Slide 21: Chiroptera II / HawkEye III Sensor Heads

## Slide 22: Dual Head DragonEye / Chiroptera II Installation

## Slide 23: HawkEye III Installation

## Slide 24: Operational Considerations: Is Lidar a Suitable Tool?
Water Clarity / Turbidity
  Seasonal
  Daily (tides / currents)
Seabed Reflectivity
  Bed type, Vegetation
Weather
  Temperature
  Rain
  Wind
  Cloud Ceiling
  Sea State
Expected Terrain & Expected Depths

## Slide 25: Survey Depth / Water Clarity
Depth penetration depends on:
  Turbidity
  Seafloor reflectance
Secchi Disk
Monthly AquaMODIS: 490nm
High Power = 2 to 3 x Secchi Depth Low Power = 1 x Secchi Depth
Seasonal Assessment
Tides/Currents

## Slide 26: Weather
Temperature
Wind
Rain
Cloud Ceiling
Sea State

## Slide 27: Additional Operational Considerations
Flight Planning Considerations Include:
  Tide range, high/low tide times
  Water quality / weather & time of year to survey
  Shape of survey area (Coastal strip or Large polygon)
  Size of survey area (maximum line lengths)
  Flying height and local terrain (Aircraft Type; Deep / Shallow Power System)
  Expected Depths (Deep / Shallow Power System)
  GPS stations and tide gauges (Single / Multi-base, SmartBASE, PPP, Tide Plan)
  Air traffic in the survey area
  Restricted airspace / special flight permits
  Operations base airport and logistics

## Slide 28: Steep Slopes Well Defined; Seamless Topo-Bathy

## Slide 29: Elliptical Scan / Multiple Returns Allow Bathy Returns Under Vegetation

## Slide 30: Elliptical Scan / Multiple Returns Allow Bathy Returns Under Vegetation

## Slide 31: Elliptical Scan and Wave Action / Seamless Topo-Bathy

## Slide 32: Sample Shallow Bathymetry Detail

## Slide 33: Sample Shallow Bathymetry Detail

## Slide 34: Elevation - Poel, Baltic Sea
8 lines
0.13m - 7.5m Depth

## Slide 35: Intensity - Poel, Baltic Sea

## Slide 36: Seagrass Delineation
Corrected Intensity
Classified Image
Raster to Vector
Classify LAS
Raw Intensity

## Slide 37: Seagrass Delineation
Corrected Intensity
Classified Image
Raster to Vector
Classify LAS
Raw Intensity

## Slide 38: Seagrass Delineation
Corrected Intensity
Classified Image
Raster to Vector
Classify LAS
Raw Intensity

## Slide 39: Seagrass Delineation
Corrected Intensity
Classified Image
Raster to Vector
Classify LAS
Raw Intensity

## Slide 40: Intensity - Poel, Baltic Sea

## Slide 41: Cross Section - Poel, Baltic Sea
20x Vertical Exaggeration
Seagrass is approximately 25cm high
Colored by Flight Line
Colored by Class

## Slide 42: RCD30 Examples
RGBN
Color Infrared
NDVI (Normalized Difference Vegetation Index)
GSD dependent on altitude: 3cm (0.1ft) to 18cm (0.6ft)

## Slide 43: Thank You
Carol Lockhart : Carol@GeomaticsDS.com